## Slide 1
Measuring Bus Frequency:
Some Fundamentals
Harold Kirkham
Pacific Northwest National Laboratory
Richland, Washington
IEEE PES GM 2019
19PESGM2927

## Slide 2
Background
We can measure frequency in many ways
  Counting zero crossings per unit time
  Fourier analysis
  Measure zero-crossing interval
  Finite-difference phase values
  and there are more choices
But those are ideas for how we measure, not what we measure
Results from the phasor measurement unit are often regarded as not useful
Why is that?
2

## Slide 3
IEEE standard C37.118.1-2011
I was one of the writers of this standard
The standard does not define frequency as a measurand—though we thought it did
  It describes a frequency error between the measured frequency and an undefined “theoretical” frequency
  It gives the analytic equation of a sinusoidal signal, the text-book definition
  And it starts out by explaining a phasor based on a sinusoid
In fact, the (2019) meaning of phasor does assume a sinusoid whose frequency is known and constant
Why measure a signal whose frequency is constant?

## Slide 4
What’s the problem?
We think about our signal in one of two ways
A function of time
A function of frequency
Idealizations! Either infinitely many sharply defined instants of time
or
infinitely long signals of defined frequencies

## Slide 5
Our intuitions are all wrong!
The concept of a “changing frequency” is a contradiction
We “imagine” the bandwidth of frequency modulation is small
Can we even put information about a changing-frequency signal on this graph?
How about a signal that does not last for ever?
frequency
time

## Slide 6
Further Problems
Having a short window of observation changes the meaning of terms like “frequency” and “spectrum”
The topic is the subject of much study, and no agreement
Two surveys identify over 250 papers on “instantaneous frequency” (!)
L. Cohen, "Time-Frequency Distributions-A Review," Proceedings of IEEE, vol. 77, no. 7, pp. 941-981, July 1989.
B. Boashash, "Estimating and Interpreting the Instantaneous Frequency of a Signal--Part 1: Fundamentals," Proceedings of IEEE , vol. 80, no. 4, pp. 520-538, April 1992.

## Slide 7
What do WE (the PMU people) do?
We observe for two cycles
We pretend we have infinitely long signals:
We ”force” them to be periodic:
We shape the window (in case the actual “frequency” is a bit off)
In other words, we use slightly inappropriate mathematics

## Slide 8
What else do WE do?
The path forward involves understanding and using measurement theory
The PMU standard has this in Appx C:
where is the th estimate of the phase angle, and so on
Is that a definition of frequency?
No, it’s a definition of how something is to be measured
Let’s look at kinds of measurement

## Slide 9
Expectations
As engineers, we expect that if we are going to measure something, we first need to define it
If we have paid attention to Kelvin, we might even expect to involve mathematics
So it seems perfectly reasonable to demand definitions
But that is for representationalist measurements
So we dig into some measurement theory

## Slide 10: Compare and contrast…
Representational | Operational
There is clear conceptual definition of measurand | Concept vaguely defined
Only a few details of the method standardized | Results depend entirely on the standardized method
Measurement able to evolve/improve over time | Measurement frozen in time by documentary standard
Alternative implementations give the same result | No alternative method sure to give the same result
Model has sufficient Degrees of Freedom to suit method | DOF not relevant: no model
Measurements are (very nearly) one to one | Measurements are usually many-to-one
Cauchy’s relation applies (linear, natural zero) | Cauchy’s relation does not apply (nonlinear, arbitrary zero)
Measurements applicable in mathematical models | Measurements not applicable in mathematical models
Concept of true value is useful | There is no single true value

## Slide 11: Compare and contrast…
Representational | Operational
Documentary standards say how well it must be measured | Documentary standards say how it must be measured
Potential for long traceability chains to unit description | Single step traceability to documentary standard
Model has sufficient Degrees of Freedom to suit method | DOF not relevant: no model
Definitional uncertainty negligible | Definitional uncertainty is everything
 | Generally possible to have long-lasting, energetic and fruitless discussion of the meaning of the measurement

## Slide 12: The answer can be found by looking at the problem from the viewpoint of a PMU
The model is the equation whose parameters you find when you measure
PMU measures amplitude, frequency, phase and ROCOF
PMU model has four independent parameters: four degrees of freedom
Signal can need more if there is “pollution”
This seems to need NINE (but maybe there should be more)

## Slide 13
The answer
If your signal has a phase jump
You cannot get that “essentially unique value”
You need a more complex model. Add more DOFs?

## Slide 14
A problem: three-phase
If steady state, no dc, two harmonics, how many degrees of freedom?
And that is just for moderate distortion!
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20

## Slide 15
What to do?
Do not
  Multiply the number of definitions in use
Maybe
  Add degrees of freedom to the model
  Filter the signal
Do
  Recognize that a different kind of solution is needed

## Slide 16
Degrees of freedom are the key
Minimum number of point-on-wave samples is given by the number of degrees of freedom in the model
But there is a problem: numbers an octave higher also work
That means the DOF situation links the problem to the sampling problem
Adding more samples to the POW system is one solution (faster sampling)
Filtering is another solution (Nyquist-frequency filter)

## Slide 17
Degrees of freedom are the key
DOF situation links the problem to constraints
That is a way of treating a measurement that is common to the work of the national metrology institute and the field application
In the NMI, you might constrain the temperature of some measurement, for example
In the field, you could filter a signal
Both are ways to reduce the DOFs needed to model the physical quantity

## Slide 18
Degrees of freedom are the key
DOF situation links the problem uncertainty calculations
Something called the “effective degrees of freedom” is involved in the calculation of coverage factor in Type A uncertainty calculations

## Slide 19
Degrees of freedom are the key
DOF situation links the problem to definitional uncertainty
The GUM defines two kinds of definitional uncertainty
a) incomplete definition of the measurand
imperfect reaIization of the definition of the measurand
Here a) means that the measurand has too few DOFs
b) means that the physical quantity has too many DOFs

## Slide 20
To measure frequency
(or anything else)
The DOF situation MUST be addressed
a) A definition with more DOFs may be possible
Reducing the number of DOFs needed to represent the signal is still a possibility
That means filtering the signal
That means an Operational measurement is needed

## Slide 21
Could there be questions?